## Slide 1
Workshop BGP untuk Jaringan Kampus
UMM (AS 65010) — ContainerLab + FRRouting
iBGP & BGP Policy — Hari 2
Internal BGP, Prefix Filtering, dan Traffic Engineering
6 Juni 2026 (Sabtu) | 09.00–17.00
BGP WORKSHOP

## Slide 2
Agenda Hari 2
SCHEDULE
01
Recap & Review LAB-01
09.00–10.45 | SESI 0–2
02
MOD-03: iBGP — 2 Border Router
11.00–12.15 | SESI 3–4
03
MOD-04: BGP Policy — Prefix Filtering
13.15–14.55 | SESI 5–6
04
MOD-05: Multi-homing & Traffic Engineering
15.10–16.50 | SESI 7–8
02 / 32

## Slide 3
SESI 0–2
Recap Hari 1 & Review LAB-01
09.00–10.45 | 105 menit

## Slide 4
SESI 0 — RECAP HARI 1
Recap Hari 1 — Apa yang Sudah Dikerjakan
Hari 1 — Ringkasan:
1. Setup ContainerLab dan FRRouting di laptop masing-masing
2. MOD-01: Kenapa UMM butuh BGP — 3 upstream, failover, traffic engineering
3. MOD-02: Konfigurasi eBGP di FRR — router bgp, neighbor, address-family, network
4. LAB-01: Peserta konfigurasi umm-border peering ke idren-pop (AS 65010 ↔ AS 65000)
Status LAB-01 — Checklist Verifikasi
Verifikasi | Perintah | Expected
Session Established | show bgp summary | State/PfxRcd = angka
Prefix UMM terkirim | show bgp ipv4 unicast neighbors ... advertised-routes | 100.72.1.0/24 dan 100.72.2.0/24
Prefix IDREN diterima | show bgp ipv4 unicast | 100.68.0.0/16 ada
Masuk routing table | show ip route bgp | 100.68.0.0/16 ada
03 / 32

## Slide 5
SESI 2 — REVIEW LAB-01
Solusi LAB-01 — Konfigurasi Lengkap
Konfigurasi umm-border
router bgp 65010
no bgp ebgp-requires-policy
bgp router-id 100.64.0.2
neighbor 100.64.0.1 remote-as 65000
neighbor 100.64.0.1 description "eBGP ke IDREN PoP"
!
address-family ipv4 unicast
network 100.72.1.0/24
network 100.72.2.0/24
neighbor 100.64.0.1 activate
exit-address-family
Null Route (wajib!)
ip route 100.72.1.0/24 null0
ip route 100.72.2.0/24 null0
Tanpa null route → PfxSnt: 0
3 Hal Sering Terlewat
1. no bgp ebgp-requires-policy
2. Null route untuk prefix UMM
3. activate di address-family
Jika lupa salah satu → review tabel common mistakes
04 / 32

## Slide 6
SESI 2 — REVIEW LAB-01
Common Mistakes LAB-01
Gejala | Root Cause | Fix
Session Active | remote-as salah (65099 bukan 65000) | Koreksi ASN, tunggu reconnect
Session Active | TCP 179 diblokir firewall | iptables -I INPUT -p tcp --dport 179 -j ACCEPT
(Policy) di State | Lupa no bgp ebgp-requires-policy | Tambahkan di router bgp 65010
PfxSnt: 0 | Null route tidak ada | Tambahkan ip route ... null0
PfxRcd: 0 | Session baru establish | clear ip bgp * soft
Router ID konflik | Keduanya auto-detect dari interface sama | Set bgp router-id eksplisit
Q&A — Pertanyaan Umum
Q: Session Established tapi prefix tidak muncul? → A: Null route hilang, atau ebgp-requires-policy
Q: Beda show bgp ipv4 unicast vs show ip route bgp? → A: BGP table vs routing table OS
Q: Kalau IDREN down? → A: Hold timer expired (90 detik), session putus, route di-withdraw
05 / 32

## Slide 7
SESI 3
iBGP: Ketika UMM Punya 2 Border Router
11.00–11.30 | MOD-03

## Slide 8
MOD-03 — iBGP
Kapan UMM Butuh iBGP?
Single Border — Tidak Butuh iBGP
Dual Border — Butuh iBGP
Key Insight
Tanpa iBGP: border-2 tidak tahu route dari IDREN yang datang ke border-1. Traffic dari user yang lewat border-2 tidak bisa mencapai tujuan di IDREN.
Dengan iBGP: border-1 berbagi route IDREN ke border-2, dan sebaliknya. Kedua border punya visibilitas penuh ke semua upstream.
Rule of thumb: Lebih dari 1 border router dengan upstream berbeda → aktifkan iBGP.
07 / 32
Border Router
AS 65010
IDREN
ISP Komersial
IIX
UMM Campus
AS 65010
IDREN
ISP Komersial
IIX
UMM Campus
AS 65010
iBGP
eBGP
eBGP
eBGP

## Slide 9
MOD-03 — iBGP
iBGP vs eBGP — Perbedaan
Atribut | eBGP | iBGP
ASN neighbor | Berbeda | Sama
TTL default | 1 (directly connected) | 255 (bisa multi-hop)
Next-hop behavior | Diubah ke IP lokal | Tidak diubah
Split horizon | Tidak ada | Ada — route iBGP tidak dikirim ke iBGP peer lain
Peer address | Interface IP | Loopback
Catatan Penting
remote-as sama dengan AS lokal = iBGP — Ini cara paling mudah membedakan eBGP vs iBGP dari konfigurasi.
Next-hop tidak berubah → masalah: Border-2 menerima route dengan next-hop IDREN yang tidak reachable. Solusi: next-hop-self — border-1 ganti next-hop ke loopback-nya sebelum kirim ke border-2.
Loopback sebagai peer address: Interface fisik bisa down, loopback selalu up selama router hidup. iBGP pakai loopback untuk keandalan.
08 / 32

## Slide 10
MOD-03 — iBGP
Masalah Next-hop di iBGP
Alur Next-hop Problem
exabgp-idren (100.64.0.1)
│ advertise 152.118.0.0/16, next-hop = 100.64.0.1
▼
border-1 (eBGP terima)
│ forward ke border-2 via iBGP
│ next-hop TETAP 100.64.0.1 ← border-2 tidak bisa reach!
▼
border-2 (iBGP terima)
× route tidak masuk routing table — next-hop unreachable
Solusi: next-hop-self
Tambahkan di konfigurasi border-1 (iBGP peer ke border-2):
neighbor 100.64.1.2 next-hop-self
Border-1 akan mengganti next-hop menjadi IP loopback-nya (100.64.1.1) sebelum mengirim route ke border-2. Sehingga border-2 bisa reach next-hop dan route masuk routing table.
09 / 32

## Slide 11
MOD-03 — iBGP
Konfigurasi iBGP — border-1 & border-2
border-1 (eBGP + iBGP)
router bgp 65010
no bgp ebgp-requires-policy
bgp router-id 100.64.1.1
neighbor 100.64.0.1 remote-as 65000
neighbor 100.64.0.1 description "eBGP ke IDREN"
neighbor 100.64.1.2 remote-as 65010
neighbor 100.64.1.2 description "iBGP ke border-2"
neighbor 100.64.1.2 update-source lo
!
address-family ipv4 unicast
network 100.72.1.0/24
network 100.72.2.0/24
neighbor 100.64.0.1 activate
neighbor 100.64.1.2 activate
neighbor 100.64.1.2 next-hop-self
exit-address-family
border-2 (iBGP only)
router bgp 65010
bgp router-id 100.64.1.2
neighbor 100.64.1.1 remote-as 65010
neighbor 100.64.1.1 description "iBGP ke border-1"
neighbor 100.64.1.1 update-source lo
!
address-family ipv4 unicast
neighbor 100.64.1.1 activate
neighbor 100.64.1.1 next-hop-self
exit-address-family
Verifikasi di border-2
show bgp ipv4 unicast → tanda i = iBGP
LocPrf 100 = Local Preference default
10 / 32

## Slide 12
MOD-03 — iBGP
Common Mistakes iBGP + Wrap-up
01
Lupa update-source lo
Session connect dari interface fisik. Saat interface down, session iBGP putus.
Fix: Selalu gunakan update-source lo untuk iBGP.
02
Loopback tidak reachable
Session stuck di Active meski konfigurasi sudah benar.
Fix: Pastikan loopback border-2 reachable dari border-1 (cek routing).
03
Lupa next-hop-self
Route diterima border-2 tapi next-hop unreachable → tidak masuk routing table.
Fix: Tambahkan next-hop-self di iBGP peer.
Wrap-up MOD-03
iBGP checklist: remote-as sama, pakai loopback, update-source lo, next-hop-self wajib
2 router: full-mesh = 1 session, tidak perlu Route Reflector
Selanjutnya: LAB-02 — konfigurasi iBGP antara border-1 dan border-2
Coffee break: 10.45–11.00 (15 menit)
11 / 32

## Slide 13
SESI 4
LAB-02: iBGP — 2 Border Router
11.30–12.15 | 45 menit

## Slide 14
SESI 4 — LAB-02
LAB-02 — iBGP: 2 Border Router
Topologi LAB-02
UMM (AS 65010)
[border-1] ──iBGP (loopback)── [border-2]
lo: 100.64.1.1/32 lo: 100.64.1.2/32
eth1: 100.64.0.2/30
│ eBGP
[exabgp-idren] AS 65000 | ~20 prefix akademik
Urutan Pengerjaan
1. Deploy: containerlab deploy -t lab02.clab.yml
2. Konfigurasi eBGP border-1 ↔ IDREN PoP (sama seperti LAB-01)
3. Konfigurasi iBGP border-1 ↔ border-2:
• update-source lo
• next-hop-self di border-1
4. Verifikasi: prefix IDREN muncul di border-2 via iBGP
Target Verifikasi
• Session border-1 ↔ exabgp-idren: Established (eBGP), PfxRcd ~22
• Session border-1 ↔ border-2: Established (iBGP)
• Di border-2: show bgp ipv4 unicast → prefix seperti 152.118.0.0/16 dengan tanda i dan next-hop 100.64.1.1
• Di border-2: show ip route bgp → 152.118.0.0/16 dengan tanda B i
12 / 32

## Slide 15
SESI 5
BGP Policy: Prefix Filtering
13.15–13.55 | MOD-04

## Slide 16
MOD-04 — BGP POLICY
Bahaya Tanpa Policy — Routing Leak
Routing Leak Scenario
IDREN ──eBGP── [Border Router UMM] ──eBGP── ISP komersial
↑
(tanpa outbound filter)
mengiklankan SEMUA route ke kedua sisi
Akibat Routing Leak
1. Tanpa outbound filter: UMM iklankan route IDREN ke ISP, dan sebaliknya
2. Traffic internet pihak lain bisa transit lewat jaringan UMM → bandwidth kampus terpakai
3. Kasus lebih serius: UMM iklankan prefix kampus lain yang bukan miliknya → blackhole atau routing hijack
Rule dasar: Outbound ke semua upstream — hanya iklankan prefix UMM sendiri (100.72.1.0/24 dan 100.72.2.0/24)
14 / 32

## Slide 17
MOD-04 — BGP POLICY
Tool Filtering — prefix-list & route-map
prefix-list (filter only)
ip prefix-list NAMA seq NOMOR
[permit|deny] PREFIX/LEN
[le LEN] [ge LEN]
! Prefix UMM sendiri
ip prefix-list OWN-PREFIX
seq 10 permit 100.72.1.0/24
seq 20 permit 100.72.2.0/24
seq 99 deny any
! Filter terlalu spesifik
ip prefix-list MAX-LEN
seq 10 deny 0.0.0.0/0 ge 25
seq 99 permit any
route-map (filter + modify)
route-map NAMA permit 10
match ip address prefix-list OWN-PREFIX
set local-preference 200
! Terapkan ke neighbor
router bgp 65010
address-family ipv4 unicast
neighbor 100.64.0.1 route-map
EXPORT-UPSTREAM out
neighbor 100.64.0.1 route-map
IMPORT-COMMON in
exit-address-family
! Perubahan tidak langsung aktif
clear ip bgp X soft
Key Points
• le (less/equal): cocok jika mask length ≤ nilai | ge (greater/equal): cocok jika mask length ≥ nilai
• Evaluasi dari seq terkecil, berhenti di match pertama | Implicit deny di akhir
• permit: prefix lolos | deny: prefix dibuang | Route-map = prefix-list + modifikasi atribut
15 / 32

## Slide 18
MOD-04 — BGP POLICY
Outbound & Inbound Policy
Outbound: Hanya Iklankan Prefix Sendiri
ip prefix-list OWN-PREFIX seq 10 permit 100.72.1.0/24
ip prefix-list OWN-PREFIX seq 20 permit 100.72.2.0/24
ip prefix-list OWN-PREFIX seq 99 deny any
route-map EXPORT-UPSTREAM permit 10
match ip address prefix-list OWN-PREFIX
! Terapkan ke SEMUA upstream neighbor dengan route-map ... out
! Verifikasi: show bgp ipv4 unicast neighbors X advertised-routes → hanya 100.72.x.x
Inbound: Filter Bogon
Prefix | Kategori
10.0.0.0/8 | RFC 1918 private
172.16.0.0/12 | RFC 1918 private
192.168.0.0/16 | RFC 1918 private
127.0.0.0/8 | Loopback
169.254.0.0/16 | Link-local
ip prefix-list BOGON seq 10 deny 10.0.0.0/8 le 32
ip prefix-list BOGON seq 20 deny 172.16.0.0/12 le 32
ip prefix-list BOGON seq 30 deny 192.168.0.0/16 le 32
ip prefix-list BOGON seq 40 deny 127.0.0.0/8 le 32
ip prefix-list BOGON seq 50 deny 169.254.0.0/16 le 32
ip prefix-list BOGON seq 99 permit any
Catatan lab: 100.64.0.0/10 (Shared address space) wajib difilter di produksi. Di LAB-03 tidak diimplementasikan karena peer link lab menggunakan subnet 100.64.x.x — memasukkan ke BOGON akan memutus session BGP.
16 / 32

## Slide 19
MOD-04 — BGP POLICY
Soft Reset & Verifikasi Policy
Tiga Varian clear ip bgp
clear ip bgp 100.64.0.1 soft ← reset inbound + outbound
clear ip bgp 100.64.0.1 soft in ← reapply inbound policy saja
clear ip bgp 100.64.0.1 soft out ← reapply outbound policy saja
Warning: clear ip bgp X (tanpa soft) → putus session, ganggu traffic!
soft-reconfiguration inbound
Wajib aktif untuk melihat received-routes:
address-family ipv4 unicast
neighbor 100.64.0.1 soft-reconfiguration inbound
Setelah ubah policy, selalu clear soft:
show bgp ipv4 unicast neighbors X received-routes ← semua yang diterima (sebelum policy)
show bgp ipv4 unicast neighbors X routes ← yang lolos policy inbound
show bgp ipv4 unicast neighbors X advertised-routes ← yang dikirim ke peer
soft out: kirim ulang Adj-RIB-Out ke peer dengan policy yang sudah diupdate
soft in: butuh soft-reconfiguration inbound aktif di konfigurasi neighbor
Rule: Setelah ubah route-map atau prefix-list → selalu clear ip bgp X soft
17 / 32

## Slide 20
MOD-04 — BGP POLICY
Common Mistakes MOD-04 + Wrap-up
# | Kesalahan | Penjelasan
1 | Route-map implicit deny | Tidak ada permit any di akhir → semua prefix yang tidak match dibuang
2 | Lupa soft-reconfig inbound | received-routes kosong, tidak bisa debug policy inbound
3 | Lupa clear soft | Policy tidak langsung aktif setelah ubah prefix-list/route-map
4 | Prefix-list urutan salah | seq 10 permit any → semua lolos, deny di bawah tidak pernah dievaluasi
5 | Outbound filter tidak lengkap | Hanya pasang ke satu upstream → lupa ke ISP/IIX → masih jadi transit
Wrap-up MOD-04
Dua alat: prefix-list (filter) + route-map (filter + modifikasi)
Outbound: hanya iklankan 100.72.1.0/24 dan 100.72.2.0/24 ke semua upstream — tidak lebih
Inbound: buang bogon dan prefix terlalu spesifik
Setelah ubah policy: selalu clear ip bgp X soft
Coffee break: 14.55–15.10 (15 menit)
18 / 32

## Slide 21
SESI 6
LAB-03: Prefix Filtering
13.55–14.55 | 60 menit

## Slide 22
SESI 6 — LAB-03
LAB-03 — Prefix Filtering
Topologi Full (4 Upstream)
UMM (AS 65010) [border-1] ←──iBGP──→ [border-2]
eth1→IDREN(AS65000) eth1→ISP-2(AS65101)
eth2→ISP-1(AS65100) eth2→IIX(AS65200)
Prefix: ~20 akademik + ~86 komersial + 1 bogon (192.168.100.0/24)
Urutan Pengerjaan
1. Deploy: containerlab deploy -t lab03.clab.yml
2. Konfigurasi eBGP + iBGP di KEDUA border (+ soft-reconfig inbound)
3. Amati kondisi sebelum policy — 192.168.100.0/24 masuk ke BGP table
4. Pasang outbound filter: hanya prefix UMM ke semua upstream
5. Pasang inbound filter: buang bogon
6. Verifikasi
Target Verifikasi
Outbound border-1:
show bgp ipv4 unicast neighbors 100.64.0.1 advertised-routes
→ Hanya 100.72.1.0/24 dan 100.72.2.0/24
Inbound bogon terfilter:
show bgp ipv4 unicast neighbors 100.64.0.5 received-routes
→ 192.168.100.0/24 ada di received-routes
show bgp ipv4 unicast
→ 192.168.100.0/24 TIDAK ada (dibuang)
19 / 32

## Slide 23
SESI 7
Multi-homing: Traffic Engineering
15.10–15.50 | MOD-05

## Slide 24
MOD-05 — TRAFFIC ENGINEERING
Outbound vs Inbound Traffic Engineering
Outbound (keluar UMM)
UMM → IDREN / ISP / IIX
Dikendalikan oleh:
Local Preference (internal AS)
Lebih tinggi = lebih diutamakan untuk keluar
Inbound (masuk ke UMM)
IDREN / ISP / IIX → UMM
Dikendalikan oleh:
AS-path prepending (iklankan ke luar)
Lebih pendek = disukai upstream untuk masuk
Target UMM — Prioritas Upstream
Upstream | Border | Outbound (LocPrf) | Inbound (Prepend) | Role
IDREN (AS 65000) | border-1 | 300 (tertinggi) | No prepend | Primary
IIX (AS 65200) | border-2 | 200 | 1× prepend | Secondary
ISP-1 (AS 65100) | border-1 | 150 | 1× prepend | Tertiary
ISP-2 (AS 65101) | border-2 | 100 (backup) | 2× prepend | Backup
21 / 32

## Slide 25
MOD-05 — TRAFFIC ENGINEERING
BGP Best-path Selection
# | Atribut | Fungsi | Kendalikan?
1 | Weight (Cisco only) | — | Tidak ada di FRR
2 | Local Preference | Outbound — internal AS | Ya ✓
3 | Locally originated | Route yang di-generate lokal | —
4 | AS-path length | Inbound — dari luar | Ya ✓
5 | Origin | IGP > EGP > Incomplete | —
6 | MED | Hint ke upstream AS yang sama | Terbatas
7 | eBGP > iBGP | Prefer route eksternal | —
8 | IGP metric | Cost ke next-hop | —
9 | Router ID | Tie-breaker terakhir | —
Local Pref lebih tinggi = lebih disukai untuk traffic keluar (outbound)
AS-path lebih pendek = lebih disukai oleh upstream untuk kirim traffic ke kita (inbound)
Dua atribut yang bisa kita kendalikan: Local Preference (#2) dan AS-path length (#4)
22 / 32

## Slide 26
MOD-05 — TRAFFIC ENGINEERING
Local Preference — Kontrol Traffic Keluar
Upstream | Border | Route-map | Local Preference
IDREN | border-1 | IMPORT-FROM-IDREN | 300 (primary)
IIX | border-2 | IMPORT-FROM-IIX | 200
ISP-1 | border-1 | IMPORT-FROM-ISP1 | 150
ISP-2 | border-2 | IMPORT-FROM-ISP2 | 100 (backup)
border-1 (IDREN=300, ISP-1=150)
route-map IMPORT-FROM-IDREN permit 10
set local-preference 300
route-map IMPORT-FROM-ISP1 permit 10
set local-preference 150
router bgp 65010
address-family ipv4 unicast
neighbor 100.64.0.1 route-map IMPORT-FROM-IDREN in
neighbor 100.64.0.5 route-map IMPORT-FROM-ISP1 in
border-2 (IIX=200, ISP-2=100)
route-map IMPORT-FROM-ISP2 permit 10
set local-preference 100
route-map IMPORT-FROM-IIX permit 10
set local-preference 200
router bgp 65010
address-family ipv4 unicast
neighbor 100.64.0.9 route-map IMPORT-FROM-ISP2 in
neighbor 100.64.0.13 route-map IMPORT-FROM-IIX in
23 / 32

## Slide 27
MOD-05 — TRAFFIC ENGINEERING
AS-path Prepending — Kontrol Traffic Masuk
Upstream | Border | Prepend | AS-path yang Dilihat Upstream
IDREN | border-1 | — | 65010 (pendek = disukai)
ISP-1 | border-1 | 1× | 65010 65010
IIX | border-2 | 1× | 65010 65010
ISP-2 | border-2 | 2× | 65010 65010 65010 (backup)
border-1 (IDREN + ISP-1)
route-map EXPORT-TO-IDREN permit 10
match ip address prefix-list OWN-PREFIX
! tidak ada prepend
route-map EXPORT-TO-ISP1 permit 10
match ip address prefix-list OWN-PREFIX
set as-path prepend 65010
! AS-path ke ISP-1: 65010 65010
border-2 (IIX + ISP-2)
route-map EXPORT-TO-IIX permit 10
match ip address prefix-list OWN-PREFIX
set as-path prepend 65010
route-map EXPORT-TO-ISP2 permit 10
match ip address prefix-list OWN-PREFIX
set as-path prepend 65010 65010
! AS-path ke ISP-2: 65010 65010 65010
24 / 32

## Slide 28
MOD-05 — TRAFFIC ENGINEERING
Failover Otomatis & Preview Hari 3
Normal (overlap prefix)
Prefix 100.121.0.0/16 tersedia dari:
• ISP-1 via border-1 (LocPrf 150)
• ISP-2 via border-2 (LocPrf 100)
ISP-1 menang — traffic keluar lewat border-1
Failover (ISP-1 down)
neighbor 100.64.0.5 shutdown di border-1
• ISP-1 path hilang dari BGP table
• 100.121.0.0/16 beralih ke ISP-2
• Hold timer 90 detik (default)
BGP best-path re-selection otomatis
Demo Failover
neighbor 100.64.0.5 shutdown
Tunggu 90 detik → show bgp ipv4 unicast 100.121.0.0/16
Path ISP-2 (LocPrf 100) sekarang menang
Preview Hari 3
• BGP Community: tagging & conditional policy
• MOD-06: Troubleshooting methodology
• LAB-05: Diagnosa broken BGP session
• Post-test & Penutupan
Common Mistakes MOD-05
• Local Pref lebih tinggi = traffic keluar (bukan masuk) — sering tertukar!
• AS-path prepend mempengaruhi path yang diiklankan → traffic masuk (bukan keluar)
• Lupa clear soft in setelah ubah IMPORT / clear soft out setelah ubah EXPORT
25 / 32

## Slide 29
SESI 8
LAB-04: Multi-homing — Traffic Engineering
15.50–16.50 | 60 menit

## Slide 30
SESI 8 — LAB-04
LAB-04 — Multi-homing: Traffic Engineering
Urutan Pengerjaan (7 Step)
1. Deploy: containerlab deploy -t lab04.clab.yml
2. eBGP + iBGP di KEDUA border + outbound filter
3. Amati tanpa local-pref — 100.121.0.0/16 path mana yang menang?
4. Pasang Local Preference: IDREN=300, IIX=200, ISP-1=150, ISP-2=100
5. Pasang AS-path prepending: IDREN no prepend, ISP-1/IIX 1×, ISP-2 2×
6. AS-path filter: prefix universitas langsung dari IDREN → LocPrf 350
7. Simulasi failover: shutdown ISP-1 → amati re-selection (~10 detik)
Target Verifikasi
Local Pref:
show bgp ipv4 unicast 100.121.0.0/16
→ Path ISP-1 (LocPrf 150) menang atas ISP-2 (100)
AS-path prepend:
show bgp ipv4 unicast neighbors 100.64.0.5 advertised-routes
→ AS-path ke ISP-1: 65010 65010 (2 entri)
AS-path filter (Step 6):
show bgp ipv4 unicast 152.118.0.0/16
→ IDREN path: LocPrf 350 (best)
Failover:
neighbor 100.64.0.5 shutdown
→ Path ISP-2 via border-2 menang
26 / 32

## Slide 31
SESI 8 — LAB-04
LAB-04 — Step 6: AS-path Filter UNIV-ID-DIRECT
Konfigurasi border-1
configure terminal
! ASN universitas Indonesia anggota IDREN
bgp as-path access-list UNIV-ID-DIRECT permit
^(7642|7654|24855|45166|45974|45958|45997)$
no route-map IMPORT-FROM-IDREN permit 10
route-map IMPORT-FROM-IDREN permit 10
match as-path UNIV-ID-DIRECT
set local-preference 350
route-map IMPORT-FROM-IDREN permit 20
set local-preference 300
end
write memory
clear ip bgp 100.64.0.1 soft in
Verifikasi Step 6
show bgp ipv4 unicast 152.118.0.0/16
→ IDREN (AS-path 7642): localpref 350, best ✓
→ ISP-1 (AS-path 7713 23700 7642): localpref 150 ✓
show bgp ipv4 unicast regexp
^(7642|7654|24855|45166|45974|45958|45997)$
→ 6+ prefix universitas, LocPrf 350 ✓
Di border-2 (iBGP):
show bgp ipv4 unicast 152.118.0.0/16
→ localpref 350, internal, best ✓
27 / 33

## Slide 32
SESI 9 — REVIEW & WRAP-UP
Review & Wrap-up Hari 2
01
LAB-02 — iBGP
Kunci: update-source lo + next-hop-self di border-1
Yang paling sering gagal: loopback tidak reachable → session Active meski config benar
02
LAB-03 — Prefix Filtering
Kunci: route-map implicit deny — selalu ada permit any di akhir prefix-list
Lupa clear soft setelah ubah policy → perubahan tidak berlaku
03
LAB-04 — Multi-homing
Kunci: Local Pref = keluar, AS-path prepend = masuk — jangan tertukar!
Konfigurasi di KEDUA border (border-1: IDREN=300/350-univ, ISP-1=150; border-2: IIX=200, ISP-2=100)
Step 6: bgp as-path access-list UNIV-ID-DIRECT → prefix universitas langsung LocPrf 350
Ringkasan Hari 2
iBGP: remote-as sama, loopback peering, update-source lo, next-hop-self wajib
BGP Policy: prefix-list + route-map, outbound filter (hanya prefix sendiri), inbound bogon filter
Multi-homing: Local Preference (outbound), AS-path prepending (inbound), failover otomatis
28 / 33

## Slide 33
Hari 2 — Selesai
SEE YOU TOMORROW
Jangan hapus lab dulu — containerlab destroy setelah diverifikasi
Lab yang belum selesai bisa dikerjakan malam ini
Pertanyaan → group chat
29 / 33